## Slide 1
2023 – 2024 Spring
EEEN 102 - Embedded Systems Programming
Final Project Presentation (30.05.2024)
First phase of open source complete Electronic Flight Instrument System (EFIS) set for UAVs, RC airplanes or backup for general aviation aircrafts.
Air Data Unit (v1.1)
Display Software (v0.1.1) Developer: İbrahim Ç. Y.
For more and further updates,
visit project’s GitHub page:

## Slide 2
Main Features of EFIS System Units:
Air Data Unit Electrical Features:
Supply voltage range: 7.5 – 25 V.
High voltage protection by varistors.
Low voltage protection by MCU brownout detection.
Separated supply lines for board and external devices.
Max 100 mA for main board and max 500 mA for external outputs.
100 mA PTC fuses on each power out.
All I/O pins (except SPI) has serial current limiting resistors.
ATMega 328P MCU @ 20 MHz
RTC chip for date and time keeping.
CR1220 battery for RTC chip.
Separated I2C lines via switch for isolating lines from each other when corruption occurs on some of lines.
Main UART for data transmission and secondary UART for GNSS module.
UART1 can capable up to 230400 bauds and has flow control pins.
UART2 can capable up to 38400 bauds.
SPI port (6 pins AVR ISP).
6 configurable general purpose I/O or analog inputs.
Air Data Unit Software Limitations:
Max 36000 ft press. alt. @ ISA conditions.
Max 1.0 Mach.
Used Programming Languages in This Project:
C/C++ used for Air Data Unit’s MCU software.
Python used for EFIS Display Software.

## Slide 3
Air Data Unit Box:
UART 1 Includes:
Serial I/O
Two I/O reserved for flow control etc.
Reset Input.
UART 2 Includes:
Serial I/O
Data Comm. LEDs
SPI (6 Pins AVR ISP)
For programming etc.
Status LED
RTC Battery
CR1220
6× I2C Channels
Avionics Bus Power In & On LED
For external outputs
Main Power In & On LED
Reset Button
General I/O Pins Includes:
6× Pins can configure as digital I/O or analog input.
1× Power output.
M3 Screw Holes
10.5 cm
9.0 cm
5.0 cm

## Slide 4
Electronic Circuit Board of Air Data Unit:
ATMega 328P Microcontroller @ 20 MHz
I2C Switch
Real Time Clock (RTC)
Supply of
Main Board
Supply of External Outputs
MCU
I2C Switch
CH 1
CH 2
CH 3
CH 4
CH 5
CH 6
I2C Bus
UART 1
UART 2
Serial
Serial & Flow Control
Pulse Circuit
Reset Signal
SPI
Reset Line
General I/O
SPI Bus
RTC
Status
Front View of Board:
Back View of Board:
Block Diagram of Circuit:
4.2 cm
8.2 cm

## Slide 5
Supply for Main Board
Supply for External Devices
Wired or Wireless Comm.
Angle of Attack Vane
Temp. Probe
Air / Ground Sense Switches
Pitot – Static Tube
Dynamic Pressure Line
Static Pressure Line
MPU6050 6-DOF Accelerometer & Gyroscope (Operated at ±8g & ±500 °/s)
QMC5883 3-DOF Magnetometer
MS4525 Differential Pressure Sensor (Max 220 KIAS)
BMP180 Pressure Sensor (Max -1500 - +29500 ft press alt.)
Air530 GNSS Receiver Supports: GPS / Beidou / Glonass / Galileo / QZSS, SBAS
Connection Diagram of Sensors and Communication Lines:
To other avionic systems.

## Slide 6
Display Software – Primary Flight Display (PFD):
Boeing-style symbology was used due to familiarity.
PFD Display Used in B737 Airliners:
Failure Flags:
Airspeed Tape
G Peaks (g)
Attitude Indicator
Slip / Skid
Indicator
P-8 Style
Vert. G Ind. (g)
Angle of Attack Indicator (°)
Altitude Tape
Altitude Indicator (ft)
Vertical Speed Indications (fpm)
Indicated Airspeed Indicator (knot)
Speed Trend
Arrow
Mach Number
Compass (°)
Altimeter Setting Indications
Compass Mode Annunciation
Turn Rate Indication (°/s)

## Slide 7
Display Software – Control Menu:
Altimeter Settings Sub-menu:
Compass Settings Sub-menu:
G Meter Sub-menu:

## Slide 8
Thank You for Listening…
For more and further updates, visit project’s GitHub page:
github.com/ibosoftnet/efis/